## Slide 1: Exercises
Analysis of protein stretching experiments

## Slide 2: Preparations
Create a working folder on your computer
  For experimenting
Create a separate folder for the Matlab files
Download files to this folder from GitHub:
  https://github.com/are-mj/OpticalTweezers
cd to the working folder
Add the Matlab files folder to the Matlab path
  addpath <folder path>

## Slide 3: Experiment files
Download the experiment files to a folder on your computer
  Alternatively, the files may be accessible on a network disk
In Matlab:
  Open datafolder.m and modify it so that folder = <data folder>

## Slide 4: Files to use in exercises
Alternatives
Use result files from your experiments.
Use a set of earlier files
    Extract files from
    OpticalTweezers/Summer school 2024/Testfiles.zip

## Slide 5: Experiment data file
seconds*4000
(minus) Force (pN)
(minus) Trap pos. A
(minus) Trap pos. B
Temperature code
Use mean of trap positions A and B
Skip first record

## Slide 6: Reading an experiment file
[t,f,x,T] = read_experiment_file(file);
Inputs:
  file: aA.txt, folder1/Aa.txt or full path
Outputs:
  t: Time (seconds since experiment start)
  f: Pulling force (pN)
  x: Trap position (nm)
  T: Temperature (˚C)

## Slide 7: Exercise 1 A: Finding rips and zips
Use read_experiment_file to read one file
Create plots of f(t) and x(t) as subplots in the same figure:
  figure; tiledlayout;
  ax1 = nexttile; plot(t,f); xlabel s; ylabel pN
  ax2 = nexttile; plot(t,x); xlabel s; ylabel nm
  linkaxes([ax1,ax2],'x’) % Couple zoom and pan in both axes
Try to locate the first few rips and zips
  Note the approximate times and force values

## Slide 8: Exercise 1 B
Run analyse_experiment for the same experiment file
  Make sure to set input ‘plotting’ to 1:
  [Trip,Tzip] = analyse_experiment(file,1);
Do the automatic rips and zips agree with yours?
If not, comment on who is probably right, and why.

## Slide 9: Exercise 1 C Δx and force shift
Zoom to one cycle having both a rip and a zip
Create variables t1 and t2 for the times for the valley on each side
  Use the datacursor tool to see the times
Create logical array ok which is true only between t1 and t2
ok = t > t1 & t < t2;
figure; plot(x(ok),f(ok))
Estimate Δx for the rip and the zip
  Tip: Use the datacursor tool
Estimate the force shifts

## Slide 10: Exercise 1 D Matlab tables
Find the row in Trip that corresponds to the rip that you estimated Δx and force shift for. How do your estimates compare with the values found automatically?
Possible reasons for any differences?

## Slide 11: The RipAnalysis app: Home tab

## Slide 12: The RipAnalysis app: f(x) tab

## Slide 13: The RipAnalysis app
Start the app by right-clicking RipAnalysis.mlapp
  Within Matlab: select Run
  In File Explorer or equivalent: select Open
Specify folders and file
  Use the buttons to browse, or paste text into the text boxes
  The data file may contain subfolder name
  The Output folder may be the same as the Data folder
    Not recommended if you are sharing the data folder with others

## Slide 14: Exerise 2: The RipAnalysis app
In this exercise we want you to use the app to go through a number of your results files
Inspect the automatically identified rip and zip events
  Remove any incorrect event
  Add any missing events
  Store results tables Trip and Tzip
The next two slides show how to remove and add events

## Slide 15: Exercise 2: Removing things
If Data folder and Data file are correct you should see a f(t) graph with rips and zips marked
Remove any disturbing data at start of end by clicking the Start or End buttons and use the crosshairs to specify new limits.
  If crosshairs are very slow to react it may help to exit Matlab and start again.
To remove a rip/zip: Zoom in so that fewer than 20 rips and zips are visible. Then click the Remove rip/zip button and select one or more events to remove from the List box
Click the Save button to store Trip and Tzip tables
Notes: Remove end: Files(1): 20230721/KC.txt Remove rip: 20230721/gA.txt (files(2))

## Slide 16: Exercise 2: Adding a rip or a zip
Find an experiment with a missing rip
  E.g. 20230724/qA.txt from Testfies.zip
Zoom in close to the missing rip and click Add Rip/Zip
Use the crosshairs to specify the time of the rip
Click the Save button again
Reload the original file
  Mark the file name
  Cut the file name (ctrl-x on Windows)
  Click somewhere outside the text box to let Matlab register the change
  Paste the file name back
Click “Recall saved changes”
Notes: 20230724/qA.txt . Files(5)

## Slide 17: Exercise 3: Fit model to data
Workflow:
  Collect all analysis result tables into TRIP and TZIP
  Select the subset you want to model (e.g. Temperature > 20)
  Prepare the input to fit_Bell_unfold.m
  Define initial values for the parameter vector
  Calculate best fit parameters for the Bell model
  Check that results look ok
    If not, try with other initial values
See Fitting models to experiment.pptx for details
If you still have time: Try to fit the Dudko model

## Slide 18: Help needed!
The Matlab programs have a single author
  Limited creativity / fantasy
  Room for improvement
  Probably many undetected bugs
Need new blood!
  Need help with program development and maintenance!
    Please contact Christian Wilson or me if you are interested.
    For my Email address, type: contact_details