## Slide 1: Fitting models to experiments
Are Mjaavatten
Optical Tweezers Summer School
Santiago, Chile
11.-15. December 2024

## Slide 2: Rip force is not the same for all experiments

## Slide 3: Rip and zip probability
The rip does not occur at the same pulling force every time
This is due to thermal fluctuations
We assume that the rip probability per unit time is a function of pulling force
If the force increases at a steady rate () it follows that the rip probability per unit force is a function of force .
This is called the rip probability density

## Slide 4: Experimental rip/zip probability estimates per unit force
If we have recorded the rip force for many events, we can count the number of rips inside force intervals (force bins) and create a histogram.
Dividing the number in each bin by the total number of rips and the bin width we get an estimate of the probability density
The models take this density as input

## Slide 5: Modelling of protein unfolding
Models use very simplified descriptions of the protein.
Most models assume:
  An energy barrier exists between the folded and the unfolded forms
  Pulling increases the energy of the protein
  The closer the energy is to the barrier value the higher is the probability that thermal fluctuations will supply an extra kick to push the protein over the barrier
  The probability that a folded protein at force F will unfold in the next short time period therefore increases with the pulling force
  The probability per second is called the unfolding rate:

## Slide 6: Bell-Evans model
The Bell-Evans model is one of the simplest models for the unfolding rate:
  is the pulling force
  is the rate at zero force
  is the distance from the zero-force equilibrium position to the barrier
  is Boltzmann’s constant
  is the absolute temperature
Evans & Ritchie, Biophys J. 72 (1997)

## Slide 7: Rip probability density function
Let be the probability that the protein remains folded at force
The rip probability density function is defined by
If the force increases at a constant rate we get:
Inserting the Bell expression for we can solve the integral in the exponent to get:
The derivation of these expressions is shown in detail in the document “Derivation of the Bell probability density expression.docx”

## Slide 8: Fitting the Bell-Evans model to experiments
The model has two unknown parameters: and
We want to find values of the parameters for the probability density function that gives the best fit to the observed probability density estimates.
  This can be done by the function lsqcurvefit from the Matlab Optimisation Toolbox
We also want to know the uncertainty of the parameter estimates.
  This can be done by the function nlparci from the Matlab Statistics and Machine Learning Toolbox
lsqcurvefit: Solve nonlinear curve-fitting (data-fitting) problems in the least-squares sense
nlparci: Nonlinear regression parameter confidence intervals

## Slide 9: Zero force unfolding rate k0
The protein we study is quite stable
This means that k0 has a very low value
When we try estimate this value directly, nlparci tends to give confidence intervals that include negative values.
Negative values of k0 do not make sense
So instead, we try to fit the base 10 logarithm of k0: log10(k0).
This is more well-behaved and gives reasonable confidence intervals.

## Slide 10: Confidence interval and standard deviation
Function nlparci gives the 95% confidence interval to
  There is 95% probability that the real parameter value is within the interval
We translate this to the more common standard deviation
  We simplify by assuming the parameter value follows a normal distribution. The interval from –1.96 to 1.96 standard deviations contains 95% of the cumulative normal distribution. Thus, the standard deviation is
    (Real statisticians may not entirely approve of this engineering approach!)

## Slide 11: Fitting results
Data for 3588 rip events from 32 experiments on the protein MJ0366.
Ref: Rivera, Mjaavatten, Smith, Baez, & Wilson (2023). Biophysical Journal, 122(3), 513-521.

## Slide 12: What do the parameters mean?
x‡ is the distance from the equilibrium position to the barrier at F = 0.
  This could in theory be measured directly or calculated from a detailed model of the protein
k0 is the unfolding rate at F = 0
  This is normally very low and cannot be observed directly
  It acts as a scaling factor on the unfolding rate expression
Protein pulling experiments are a simple(?) way of observing these properties

## Slide 13: The Dudko model
Dudko et al. proposed a generalisation of the Bell model
The unfolding rate is
This model introduces two extra parameters
  has to do with the form of the energy potential
  is the height of the barrier at .
Dudko, Hammer and Szabo (Phys. Rev. Lett. 96. 2006)

## Slide 14: In this case the two models are equally good

## Slide 15: Over-parameterization
There is a limit to how many parameters you can meaningfully determine from your data.
With four parameters I can fit an elephant, and with five I can make him wiggle his trunk.
John Von Neumann (1903-1957)
American mathematician, physicist and computer scientist
It is a paradox that artificial intelligence models may use billions of parameters!

## Slide 16: Why use the Dudko model?
Can potentially give extra information
  Barrier height
Problem:
  The standard deviation is larger than the value estimate!!!
  Even if we freeze the value of .
Cause of problem:
  Dudko often gives good fits for a wide range of values
  Then the extra information is meaningless! (over-parameterisation)
The Dudko model with is equivalent to the Bell model

## Slide 17: When is the Dudko model relevant?
For many data sets, the Dudko model may give a better fit than the Bell model
Then the standard deviation of is much smaller
And the result of the fitting is more meaningful
Morale:
  Check the standard deviation of identified parameters
  If one or more standard deviations are very large, use the Bell model

## Slide 18: Model fitting workflow
Collect all analysis result tables into TRIP and TZIP
Select the subset you want to model (e.g. Temperature > 20)
Prepare the input to fit_Bell_unfold.m
Define initial values for the parameter vector
Calculate best fit parameters for the Bell (or Dudko) model
Check that results look ok
  If not, try with other initial values

## Slide 19: Collect analysis result tables
Make a list of all results files for your protein
  Regardless of temperature, pulling speed or whatever
    You can easily extract subsets later
Aid to creating the file list:
  Collect all experiment subfolders in a string array:
    folders = ["subfolder1","subfolder2","subfolder3"];
  Create array of experiment file names:
    files = experiment_filenames(folders);
  Requires that you have created the file datafolder.m

## Slide 20: Collect analysis result tables (2)
If you have not used the RipAnalysis app to modify results
  You may use the automatic analysis result without modifucation
  [TRIP,TZIP] = analyse_many(files);
  This runs analyse_experiment for all the files and collects the Trip and Tzip tables into TRIP and TZIP
If you have modified results in RipAnalysis for one or more files:
  [TRIP,TZIP] = collect_tables(files);
    Reads tables created by the RipAnalysis app where available
    For the rest, calculates tables using the analyse_experiment function

## Slide 21: Select subsets
Logical arrays can be used to select subsets of tables or arrays
Example: extract the elements of numerical array x that are > 0:
  >> x = [6,-3,1,-6,3,-4,-7,4,5,0];
  >> positive = x>0
  positive =
  1×10 logical array
  1 0 1 0 1 0 0 1 1 0
  >> selection = x(positive)
  selection =
  6 1 3 4 5

## Slide 22: Select subsets (2)
Create logical arrays for the conditions of interest
  Example: Experiments with T <20˚C and Pulling speed < 200nm/s ok = TRIP.Temperature<20 & TRIP.Pullingspeed < 200;
  ok = 1 where the condition is true, 0 elsewhere
Use the logical array ok to extract only the relevant data:
  F = TRIP.Force(ok);
Pullingspeed is calculated directly from the trap position and may be more accurate than Fdot.
"omitmissing"
"omitmissing"

## Slide 23: Prepare input to fit_Bell_unfold and fit_Dudko_unfold
[theta,theta_std] =... fit_Bell_unfold(pd_obs,edges,Tmean,Fdot,theta0);
pd_obs and edges are calcuated by function probdens:
  dF = 2; % distance between force bin edges (bin width)
  [pd_obs,edges] = probdens(F(ok),dF); pd_obs(i) is the observed probability for unfolding (or refolding) in the bin from edges(i) to edges(i+1) divided by the bin width
Tmean = mean(TRIP.Temperature(ok),"omitmissing");
Fdotmean = mean(TRIP.Fdot(ok),"omitmissing");
theta0 = [dx0;log10k0] is the initial guess for the parameter vector
  More on theta0 later

## Slide 24: Prepare input (2)
Inspect the observed probability density:
F_list = (edges(1:end-1)+edges(2:end))/2; % force bin midpoints
figure; bar(F_list,pd_obs,1);
Data from Testfiles.zip in
https://github.com/are-mj/OpticalTweezers

## Slide 25: Initial parameter guess
The optimisation function lsqcurvefit tries to find parameter values that minimise the difference between calculated and observe probability densities
The initial parameter vector tells lsqcurvefit where to start the search
Optimisation may be tricky:
The search may easily fail if initial values are far from the solution

## Slide 26: Initial parameter guess (2)
The Bell and Dudko model parameter may create problems for the fitting process because it may vary by orders of magnitude
To improve robustness, we replace it by the base 10 logarithm lg. The parameters are then dx = and lgk0 =
Guesses for parameters k0 = and dx = that often work for the Bell model are
  dx0 = 2;lgk0 = -3; theta0 = [dx0;lgk0];
For Dudko:
  dG0 = 80;dx0 = 2;lgk0 = -3; theta0 = [dG0;dx0;lgk0];

## Slide 27: Calculate best fit parameters
Function Bell_unfold_probability calculates the probability density distribution for a given parameter vector
Function fit_Bell_unfold calls this function repeatedly, searching for the parameter set that best fits the observed distribution;
  [theta,theta_std] = fit_Bell_unfold(pd_obs,edges,Tmean,Fdotmean,theta0);
Print resulting parameters:
  fprintf("x‡ = %.2fnm ± %.2g\n",theta(1),theta_std(1))
  fprintf("lg(k0) = %.2f ± %.2g\n",theta(2),theta_std(2))
  x‡ = 1.40nm ± 0.068
  lg(k0) = -1.92 ± 0.15

## Slide 28: Inspecting the result
Create a set of 100 force values for the x axis:
  F_plot = linspace(edges(1),edges(end));
Calculate and plot the probability density a:
  pd = Bell_unfold_probability(theta,F_plot,Tmean,Fdotmean);
  hold on; % To keep the bar graph
  plot(F_plot,pd,'r','linewidth',2);
Add info to the plot:
  xlabel("Force (pN)")
  ylabel("Probability density (pN^-^1)")
  title("Probability density for T>20\circC")
  legend("Observed","Bell model","location","northwest")
\circ is LaTex for °

## Slide 29: Inspecting the result
The curve is a good fit to the data
If initial parameter guesses are bad, the red curve is usually close to zero.
All the Matlab commands in the previous slides are collected in the file model_fitting_demo.m

## Slide 30: Units
Optical Tweezers experiments require some special units:
Length: 1nm = 10-9m
Force: 1pN = 10-12N
Energy per molecule: nm·pN = 10-21J = 1zJ (zettaJoule)
Avogadro constant: NA = 6.02214 ×1023 molecules/mol
Energy per mol: 1nm·pN · NA= 602.214J/mol = 602.214 (J/mol) / 4184J/kcal = 0.1439 kcal/mol
Boltzmann constant: kB = 1.381 J ×10-23J/K = 0.01381 nm·pN /K