## Slide 1: Fitting models to experiments
Are Mjaavatten
Optical Tweezers Summer School
Santiago, Chile
11.-15. December 2024

## Slide 2: Rip force is not the same for all experiments

## Slide 3: Rip and zip probability
The rip does not occur at the same pulling force each time
This is due to thermal fluctuations
We assume that the rip probability per unit time is a function of pulling force
If the force increases at a steady rate () the rip probability per unit force is a function of force .
This is called the rip probability densiy

## Slide 4: Experimental rip/zip probability estimates per unit force
If we have recorded the rip force for many events with similar parameters, we can count the number of rips inside force intervals (force bins) and create a histogram.
Dividing the number in each bin by the total we get an estimate of the probability density
The models take this density as input

## Slide 5: Modelling of protein unfolding
Models use very simplified descriptions of the protein.
Most models assume:
  An energy barrier exists between the folded and the unfolded forms
  Pulling increases the energy of the protein
  The closer the energy is to the barrier value the higher is the probability that thermal fluctuations will supply an extra kick to push the protein over the barrier
  The probability that a folded protein at force F will unfold in the next short time period therefore increases with the pulling force
  The probability per second is called the unfolding rate:

## Slide 6: Bell-Evans model
The Bell-Evans model is one of the simplest models for the unfolding rate:
  is the pulling force
  is the rate at zero force
  is the distance from the zero-force equilibrium position to the barrier
  is Boltzmann’s constant
  is the absolute temperature
Evans & Ritchie, Biophys J. 72 (1997)

## Slide 7: Rip probability density function
The probability that the rip will take place in a small force interval from to is , where is the probability that the protein has not already unfolded.
If the pulling force increases with time at a steady rate :
Inserting the Bell expression for we can solve the integral in the exponent to get:
The derivation of these expressions is shown in detail in the document “Derivation of the Bell probability density expression.docx”

## Slide 8: Experimenters may vary the conditions between experiments
It is usually of interest to study how experimental parameters influence the experiment results
The figure shows temperature and pulling speed for a large set of experiment data
Data for 3588 rip events from 32 experiments on the protein MJ0366.
Ref: Rivera, Mjaavatten, Smith, Baez, & Wilson (2023). Biophysical Journal, 122(3), 513-521.

## Slide 9: Fitting the Bell-Evans model to experiments
The model has two unknown parameters: and
We want to find values of the parameters that give the best fit of probability density function to the observed probability density estimates.
  This can be done by the function lsqcurvefit from the Matlab Optimisation Toolbox
We also want to know the uncertainty of the parameter estimates.
  This can be done by the function nlparci from the Matlab Statistics and Machine Learning Toolbox
lsqcurvefit: Solve nonlinear curve-fitting (data-fitting) problems in the least-squares sense
nlparci: Nonlinear regression parameter confidence intervals

## Slide 10: Fitting results
Data for 3588 rip events from 32 experiments on the protein MJ0366.
Ref: Rivera, Mjaavatten, Smith, Baez, & Wilson (2023). Biophysical Journal, 122(3), 513-521.

## Slide 11: What do the parameters mean?
x‡ is the distance from the equilibrium position to the barrier at F = 0.
  This could in theory be measured directly or calculated from a detailed model of the protein
k0 is the unfolding rate at F = 0
  This is normally very low and cannot be observed directly
  It acts as a scaling factor on the unfolding rate expression
Protein pulling experiments are a simple(?) way of observing these properties

## Slide 12: The Dudko model
Dudko et al. proposed a generalisation of the Bell model
The unfolding rate is
This model introduces two extra parameters
  has to do with the form of the energy potential
  is the height of the barrier at .
Dudko, Hammer and Szabo (Phys. Rev. Lett. 96. 2006)

## Slide 13: In this case the two models are equally good

## Slide 14: Why use the Dudko model?
Can potentially give extra information
  Barrier height
Problem:
  The standard deviation is larger than the value!!!
Cause of problem:
  Dudko gives good fits for a large range of values
  The extra information is meaningless!
The Dudko model with is equivalent to the Bell model

## Slide 15: When is the Dudko model relevant?
For many data sets, the Dudko model may give a better fit than the Bell model
Then the standard deviation of is much smaller
And the result of the fitting is more meaningful
Morale:
  Check the standard deviation of identified parameters
  If one or more standard deviations are very large, use the Bell model

## Slide 16: Model fitting workflow
Collect all experimental results in Matlab tables TRIP and TZIP
Select the subset you want to model
Prepare the input
  pd_obs, edges: observed probabilities between bin edges
  Tmean, Fdotmean: Mean values of temperature and force rate
Define initial values for the parameter vector
Calcuate bets fit parameters for the Bell or Dudko model
Check that results look ok
  If not, try with other initial values

## Slide 17: Creating summary tables
Collect all experiment subfolders in a string array:
  folders = ["subfolder1","subfolder2","subfolder3"];
Create array of experiment file names:
  files = experiment_filenames(folders);
Merge Trip and Tzip tables for all experiment files.
  [TRIP,TZIP] = collect_tables(files,outputfolder);
    Default outputfolder is the one defined in the app
  Reads tables created by the RipAnalysis app where available
  For the rest, calculates automatic tables using the analyse_experiment function
collect_tables can also be used without the app

## Slide 18: Select subsets
Use logical arrays to select the data subsets of interest
  Example: Experiments with T >20˚C and Pulling speed > 500nm/s ok = TRIP.Temperature>20 & TRIP.Pullingspeed > 500;
  ok = 1 where the condition is true, 0 elsewhere
Example of how logical arrays can be used
"omitmissing"
"omitmissing"
>> x = [5 3 -2 6 -4 1];
>> y = [1 2 3 4 5 6];
>> positive_x = x>0
positive_x =
1×6 logical array
1 1 0 1 0 1
>> y(positive_x)
ans =
1 2 4 6

## Slide 19: Prepare input
Use the logical array to extract only the relevant data:
  F = TRIP.Force(ok);
  Tmean = mean(TRIP.Temperature(ok),"omitmissing");
  Fdotmean = mean(TRIP.Fdot(ok),"omitmissing");
Function probdens will calculate the observed probability density array:
  dF = 1; % distance between force bin edges
  [pd_obs,edges,n_obs] = probdens(force,dF); pd_obs(i) is the mean probability density for unfolding (or refolding) in the interval from edges(i) to edges(i+1)
  n_obs is the number of rips or zips

## Slide 20: Plot observed probability density
Find mid-points of the force bins
  F_list = (edges(1:end-1)+edges(2:end))/2;
Create bar plot with bar width equal the bin width:
  figure; bar(F_list,pd_obs,dF);

## Slide 21: Initial parameter values
The optimisation function lsqcurvefit tries to find parameter values that minimise the difference between calculated and observe probability densities
The initial parameter vector tells lsqcurvefit where to start the search
Optimisation may be tricky:
The search may easily fail if initial values are far from the solution

## Slide 22: Initial parameter values
The Bell and Dudko model parameter may create problems for the fitting process because it my vary by orders of magnitude
To improve robustness we replace it by the base 10 logarithm lg. The parameters are then dx = and lgk0 =
Guesses for parameters k0 = and d = that often work for the Bell model are
  dx0 = 2;lgk0 = -3; theta0 = [dx0;lgk0];
For Dudko:
  dG0 = 80;dx0 = 2;lgk0 = -3; theta0 = [dG0;dx0;lgk0];

## Slide 23: Fitting the Bell model
Function Bell_unfold_probability calculates the probability density distribution for a given parameter vector
Function fit_Bell_unfold calls this function repeatedly, searching for the parameter set that best fits the observed distribution;
  [theta,theta_std] = fit_Bell_unfold(pd_obs,edges,Tmean,Fdotmean,theta0);
Print results:
  fprintf("x‡ = %.2fnm ± %.2g\n",theta(1),theta_std(1))
  fprintf("lg(k0) = %.2f ± %.2g\n",theta(2),theta_std(2))
  x‡ = 1.40nm ± 0.068
  lg(k0) = -1.92 ± 0.15

## Slide 24: Inspecting the result
Create a set of 100 force values for the x axis:
  F_plot = linspace(edges(1),edges(end));
Calculate and plot the probability density a:
  pd = Bell_unfold_probability(theta,F_plot,Tmean,Fdotmean);
  hold on;
  plot(F_plot,pd,'r','linewidth',2);
Add info to the plot:
  xlabel("Force (pN)")
  ylabel("Probability density (pN^-^1)")
  title("Probability density for T>20\circC")
  legend("Observed","Bell model","location","northwest")
\circ is LaTex for °

## Slide 25
All the Matlab commands in the previous slides are collected in the file model_fitting_demo.m

## Slide 26: Units
Optical Tweezers experiments require some special units:
Length: nm = 10-9m
Force: pN = 10-12N
Energy per molecule: nm·pN = zJ = 10-21J
NA = 6.02214 ×1023 molecules/mol
Energy per mol: 1nm·pN · NA= 602.214J/mol = 602.214 J/mol / 4184J/kcal = 0.1439 kcal/mol
Boltzmann’s constant: kB = 1.381 J ×10-23J/K = 0.01381 nm·pN /K